## Slide 1: Fault Tolerant Infective Countermeasure for AES
Sikhar Patranabis and Abhishek Chakraborty
Under the supervision of
Dr. Debdeep Mukhopadhyay
Secured Embedded
Architecture Laboratory (SEAL)

## Slide 2: Outline
Introduction
Differential Fault Analysis (DFA)
Countermeasures to DFA – Detection vs Infection
Infective Countermeasures – Formal Proofs of Security
Infective Countermeasures - Loopholes
Fault Tolerant Implementation of Infective Countermeasures
Conclusions

## Slide 3: Introduction : Fault Analysis and Countermeasures
Fault Analysis
Adversary injects faults into cryptosystems and analyzes the faulty output to recover the key
Easy to perform, does not require high end equipment
Must design efficient countermeasures against fault attacks
Weakens even mathematically robust cryptosystems

## Slide 4: Fault Attacks : A Brief Overview
Introduction of faults in the normal execution of cryptographic algorithms and analysis of faulty output to obtain the key
First conceived in 1996 by Boneh, Demillo and Lipton
E. Biham developed Differential Fault Analysis (DFA) of DES
Today there are numerous examples of fault analysis of block ciphers such as AES under a variety of fault models and fault injection techniques
Popular Fault Injection Techniques – Clock Glitches, Voltage Glitches, EM and Optical Injection Techniques

## Slide 5: Differential Fault Analysis (DFA)
Comparison of fault-free and faulty ciphertexts
Important factors are fault location and fault model
Fault Location:
  Data Path
  Key Schedule
Fault Model:
  Bit Faults
  Byte Faults

## Slide 6: DFA of AES: State of the Art
Single fault for unique key recovery, Key Space: 28 , Time Complexity: 232
Tunstall, Mukhopadhyay, Ali (WISTP 2011)
2011
2 faults for unique key recovery, Time Complexity: 232
Mukhopadhyay (AfricaCrypt 2009)
2009
2003
Demonstrated attack possibility with a single fault
Ali, Mukhopadhyay (eprint 2011) further reduced the time complexity to 230
Piret et. al. (CHES 2003)
2 faults for unique key recovery, Time Complexity: 240

## Slide 7: Countering DFA
Countermeasures to DFA
Detection Based Countermeasures
Vulnerable to attacks on the comparison step
Vulnerable to biased fault attacks
Infection Based Countermeasures
No formal proofs of security
Vulnerable to flow sequence changes

## Slide 8: Detection Based Countermeasures
Also known as Concurrent Error Detection (CED) techniques
Use various kinds of redundancy to detect faults
Vulnerable to attacks in the comparison step itself
Vulnerable to biased fault attacks

## Slide 9: The Basic Principle of CEDs

## Slide 10: Examples of CED
Information Redundancy – Robust Codes
Time Redundancy
Hardware Redundancy
Hybrid Redundancy - REPO
Source : Guo et. al. , Security analysis of concurrent error detection against differential fault analysis – Journal of Cryptographic Engineering, 2014

## Slide 11: Infective Countermeasures
The main initial idea behind infective countermeasures was to diffuse the impact of the fault such that even if the adversary were to attack the comparison step, the state would still be affected

## Slide 12: The Infection Mechanism
Source : Lomne et. al. , On the Need of Randomness in Fault attack Countermeasures – Application to AES, FDTC 2012

## Slide 13: Infective Countermeasures : State of the Art
Tupsamudre et. al. proposed a randomized infective countermeasure in CHES 2014
Since 2014
Gierlichs et. al. proposed in LatinCrypt 2012 a randomized infective countermeasure that totally does away with explicit consistency checks by clever use of random and dummy rounds
2012-2014
Prior to
2012
Fournier et. al. and Joye et. al. suggested infective countermeasure schemes using deterministic diffusion functions
Proved to be inherently insecure by Lomne et. al. in FDTC 2012
Propagation of faults prevents an attacker from being able to conduct any fault analysis of corrupted ciphertexts
Proved to be insecure by Battistello et. al. in FDTC 2013 and Tupsamudre et. al. in CHES 2014
Addresses several pitfalls of the earlier infective countermeasure scheme
Does not provide any formal proofs of security
Does not consider attacks where the execution order of instructions could be changed
Used consistency checks between cipher and redundant computations

## Slide 14: CHES 2014 Infective Countermeasure

## Slide 15: CHES 2014 Countermeasure (Contd.)
Correct Computation
Faulty Computation

## Slide 16: Unexplored Territory-1
Formal Proof of Security
  A frequent criticism of infective countermeasures - no explicit formal proof of security

## Slide 17: Unexplored Territory-||
The countermeasure provides security against fault attacks that target the state registers
What about faults that target the execution order of instructions instead?
For instance instruction skip attacks

## Slide 18: Information Theoretic Proof of Security
Single Fault Injection
Infection upon detection of fault destroys any correlation between output differential ∆ and key K
Hence ∆ and K are independent

## Slide 19: Security Proofs (contd.)
Multiple Fault Injection
  The adversary must introduce the same fault in a redundant-cipher round pair
  Not easy due to the presence of random intermediate dummy rounds in between
The Attack Probability for 30 Dummy Rounds

## Slide 20: Security Proofs (contd.)
The Evaluation
We focus on the event e’ where an adversary introduces the same fault in a redundant-cipher round pair
Set of faults possible for key

## Slide 21: The Instruction Skip Fault Model
The adversary can skip an instruction
Equivalent to replacing instruction by a NOP
Practically achievable on a variety of architectures
  8-bit AVR microcontrollers
  32-bit ARM9 processor
  32-bit ARM Cortex-M3 processor
Variety of injection techniques possible - Clock glitches, EM Glitches, Voltage glitches and Laser shots

## Slide 22: The Attack Idea
What if the adversary skips this step??

## Slide 23: The Attack Procedure
Skip the increment of the round counter after the final redundant round
The last cipher round is replaced by a spurious redundant round
The adversary obtains the output of the 9th round
Replaced by a Redundant Round

## Slide 24: The Information Leakage
Consider the event e that the attacker successfully performs the instruction skip to recover the key

## Slide 25: The Loop Holes
Fixed ordering of redundant and cipher rounds
Fault in the redundant round is only detected in the next cipher round
No check if a redundant round being executed is valid
Round counter is not validated

## Slide 26: Modified Infective Countermeasure
The relative ordering of cipher and redundant rounds is randomized
The intermediate output after each odd computation round is masked
Penultimate computation could be redundant or cipher
In either scenario, instruction skip gives a masked output that has no correlation with the key

## Slide 27: Instruction Skips on the Modified Countermeasure
Must skip two instructions now – the round counter increment as well as the masking steps in two separate rounds
Practically feasible second order fault attack?

## Slide 28: Some Comparisons

## Slide 29
But what about other Instruction Skip instances ??

## Slide 30: Fault Tolerance at the Instruction Level
Injection of faults in two instructions separated by only a few clock cycles is difficult to achieve in practice
Rewrite compiler generated assembly code by replacing each instruction by a sequence of one or more idempotent instructions
All instructions belong to the x86 instruction set and have uniform size of 32 bits
Provides protection against instruction skip attacks in general

## Slide 31: Sample Instruction Replacement Sequences

## Slide 32: Sample Instruction Replacement Sequences

## Slide 33: Impact on Code Size

## Slide 34: Simulation Studies

## Slide 35: Experimental Set-Up

## Slide 36: Experimental Results

## Slide 37: Conclusions
Infective countermeasures thwart DFA using single and double fault injections that do not alter the flow sequence
Infective countermeasures are vulnerable to instruction skip attacks unless properly implemented
Fault tolerance can be achieved at the instruction level using idempotent instructions

## Slide 38: Disseminations
S.Patranabis, A.Chakraborty and D.Mukhopadhyay. Fault Tolerant Infective Countermeasure for AES. In Security, Privacy, and Applied Cryptographic Engineering (SPACE) 2015

## Slide 39
Thank You for your attention!!