## Slide 1: BMC: A quick recap
Basic steps:
  We unfold the property into Boolean clauses over different time steps
  We unfold the state machine into Boolean clauses over the same number of time steps
  We check whether the clauses are together satisfiable

## Slide 2: Example: Priority Arbiter
Implementation
Property:
When r1 is high, g1 must be asserted for the next two cycles
In Linear Temporal Logic: G( r1  Xg1  XXg1 )
Specification
r1
r2
g1
g2
Initial state: g1=0, g2=1

## Slide 3: Example: Priority Arbiter
Transition Relation:
g2  r2   r1   g1
g1  r1
Property: G( r1  Xg1  XXg1 )
Negate property: F( r1  (Xg1  XXg1) )
Unfold transition relation one step at a time and check whether a
witness for the negated property exists
Strategy:
r1
r2
g1
g2
Initial state: g1=0, g2=1

## Slide 4: Variables in Temporal Worlds
Arbiter
r1
r2
g1
g2
If r1 is true in a cycle then g1 has to be
true for the next two cycles
r10
r20
g10
g20
r11
r21
g11
g21
r12
r22
g12
g22
time:0
time:1
time:2
Temporal worlds
t [ r1t  g1t+1  g1t+2 ]

## Slide 5: Example: Bound=2
Clauses from Transition Relation:
C11: r20   r10   g10  g21
C21: r10  g11
r1
r2
g1
g2
Clauses from Initial State:
I: g20  g10
Is there a witness of length=2?
Clauses from Property: F( r1  (Xg1  XXg1) )
Z1: r10   g11
SAT Check: Is Z1  I  C11  C21 satisfiable?
Answer: No, since Z1 conflicts with C21

## Slide 6: Example: Bound=3
Clauses from Transition Relation:
C11, C21: from previous iteration
C12: r21   r11   g11  g22
C22: r11  g12
r1
r2
g1
g2
Clauses from Initial State:
I: g20  g10
Is there a witness of length=3?
Clauses from Property: F( r1  (Xg1  XXg1) )
Z2: (r10  ( g11  g12 ))  (r11  g12)
SAT Check: Is Z2  I  C11  C21  C12  C22 satisfiable?
Yes: Witness: r10 = 1, r11 = 0, g11 = 1, g12 = 0, rest are don’t cares
Conclusion: We have found a bug!!

## Slide 7: Formal Methodology
Bound on path length k
Clauses describing the system M :
- Initial state : I(s1)
- Unrolled transition relation : Λi=1..k-1 T(si , si+1)
Loop clause loopik = Vj=i..k T(sk , sj)
[f]i,k means that temporal property f is true at runs starting from si and provable in k BMC iterations.
For the property f to hold on the system M Λ [f]1,k must be valid.

## Slide 8: Translation of LTL to SAT
Xf is true at state si , iff f is provable starting from si+1
[ X f ]i,k = (i < k ) Λ [ f ]i+1,k
Ff is true in state si , iff f is provable within k iterations from some future state sj
[ F f ]ik = Vj=i..k [ f ]j,k
Gf is true in state si , iff f is true at all states reachable in k iterations and all paths loop
[ G f ]i,k = Λj=i..k [ f ]j,k Λ loopik
f U g is true at si , iff g is provable from some state reachable within k iterations and f is provable from all preceding states within k iterations
[ f U g ]i,k = Vj=i..k( [ g ]j,k Λ Λn=i..j-1[ f ]n,k)