## Slide 1
Bounded Model Checking
Pallab Dasgupta
Professor, Dept. of Computer Science & Engg.,
Professor-in-charge, AVLSI Design Lab,
Indian Institute of Technology Kharagpur
Testing & Verification
Dept. of Computer Science & Engg, IIT Kharagpur

## Slide 2: Bounded Model Checking (BMC)
<number>
Broad Methodology
  We construct a Boolean formula that is satisfiable iff the underlying state transition system can realize a finite sequence of state transitions that satisfy the temporal property we are trying to validate
  We use powerful SAT solvers to determine the satisfiability of the Boolean formula
  The bound may be increased incrementally until we reach the diameter of the state transition graph

## Slide 3: Requirements
<number>
Specification in temporal logic.
System as a finite state machine.
Bound, k, on path length.
  In bounded model checking, only paths of bounded length k or less are considered.

## Slide 4: BMC: Translation to SAT
<number>
We unfold the property into Boolean clauses over different time steps
We unfold the state machine into Boolean clauses over the same number of time steps
We check whether the clauses are together satisfiable

## Slide 5: Example: Priority Arbiter
<number>
Implementation
Property:
When r1 is high, g1 must be asserted for the next two cycles
In Linear Temporal Logic: G( r1  Xg1  XXg1 )
Specification
r1
r2
g1
g2
Initial state: g1=0, g2=1

## Slide 6: Example: Priority Arbiter
<number>
Transition Relation:
g2  r2   r1   g1
g1  r1
Property: G( r1  Xg1  XXg1 )
Negate property: F( r1  (Xg1  XXg1) )
Unfold transition relation one step at a time and check whether a
witness for the negated property exists
Strategy:
r1
r2
g1
g2
Initial state: g1=0, g2=1

## Slide 7: Variables in Temporal Worlds
<number>
Arbiter
r1
r2
g1
g2
If r1 is true in a cycle then g1 has to be
true for the next two cycles
r10
r20
g10
g20
r11
r21
g11
g21
r12
r22
g12
g22
time:0
time:1
time:2
Temporal worlds
t [ r1t  g1t+1  g1t+2 ]

## Slide 8: Example: Bound=2
<number>
Clauses from Transition Relation:
C11: r20   r10   g10  g21
C21: r10  g11
r1
r2
g1
g2
Clauses from Initial State:
I: g20  g10
Is there a witness of length=2?
Clauses from Property: F( r1  (Xg1  XXg1) )
Z1: r10   g11
SAT Check: Is Z1  I  C11  C21 satisfiable?
Answer: No, since Z1 conflicts with C21

## Slide 9: Example: Bound=3
<number>
Clauses from Transition Relation:
C11, C21: from previous iteration
C12: r21   r11   g11  g22
C22: r11  g12
r1
r2
g1
g2
Clauses from Initial State:
I: g20  g10
Is there a witness of length=3?
Clauses from Property: F( r1  (Xg1  XXg1) )
Z2: (r10  ( g11  g12 ))  (r11  g12)
SAT Check: Is Z2  I  C11  C21  C12  C22 satisfiable?
Yes: Witness: r10 = 1, r11 = 0, g11 = 1, g12 = 0, rest are don’t cares
Conclusion: We have found a bug!!

## Slide 10: Formal Methodology
<number>
Bound on path length k
Clauses describing the system M :
- Initial state : I(s0)
- Unrolled transition relation : Λi=0..k-1 ρ(si , si+1)
Loop clause loopik = Vj=i..k ρ(sk , sj)
[f]i,k means that temporal property f is true at state si .
For the property f to hold on the system M Λ [f]i,k must be satisfiable.

## Slide 11: Translation of LTL to SAT
<number>
[ X f ]i,k = (i < k ) Λ [ f ]i+1,k
[ F f ]I,k = Vj=i..k [ f ]j,k
[ G f ]i,k = Λj=i..k [ f ]j,k Λ loopik
[ f U g ]i,k = Vj=i..k( [ g ]j,k Λ Λn=i..j-1[ f ]n,k)

## Slide 12: Advantages
<number>
Able to handle larger state spaces as compared to BDD’s.
Takes advantage of several decades of research on efficient SAT solvers.
The witness/counterexample produced are usually of minimum possible length, making them easier to understand and analyze.

## Slide 13: Limitations of BMC
<number>
Sound but not complete
  Works for a bounded depth
  In order to have a complete procedure, we need to run it at least up to the diameter (unknown) of the transition system
For larger depths the number of clauses can grow rapidly, thereby raising capacity issues
Nevertheless, SAT-based FPV tools can handle much larger designs as compared to BDD-based tools