## Slide 1
MultiDimensional Arrays
<number>

## Slide 2
TwoDimensional Arrays
We have seen that a oneDimensional array can store a list of values.
Many applications require us to store a table of values – implemented as a 2D array.
75 | 82 | 90 | 65 | 76
68 | 75 | 80 | 70 | 72
88 | 74 | 85 | 76 | 80
50 | 65 | 68 | 40 | 70
Student 1
Student 2
Student 3
Student 4
Subject 1
Subject 2
Subject 3
Subject 4
Subject 5
2
Notes: 37

## Slide 3
TwoDimensional Arrays
The table contains 4 rows with 5 elements each.
  The table can be regarded as a matrix / 2D array consisting of 4 rows and 5 columns.
75 | 82 | 90 | 65 | 76
68 | 75 | 80 | 70 | 72
88 | 74 | 85 | 76 | 80
50 | 65 | 68 | 40 | 70
Student 1
Student 2
Student 3
Student 4
Subject 1
Subject 2
Subject 3
Subject 4
Subject 5
3
Notes: 37

## Slide 4
Declaring 2D Arrays
General form:
type array_name[row_size][column_size];
Examples:
int marks[4][5];
float sales[12][25];
double matrix[100][100];
First index indicates row, second index indicates column.
Both row index and column index start from 0 (similar to what we had for 1D arrays)
4
Notes: 37

## Slide 5
Declaring 2D Arrays
int m[4][5];
m[0][0] | m[0][1] | m[0][2] | m[0][3] | m[0][4]
m[1][0] | m[1][1] | m[1][2] | m[1][3] | m[1][4]
m[2][0] | m[2][1] | m[2][2] | m[2][3] | m[2][4]
m[3][0] | m[3][1] | m[3][2] | m[3][3] | m[3][4]
Row 0
Row 1
Row 2
Row 3
Column 0
Column 1
Column 2
Column 3
Column 4
5

## Slide 6
Accessing Elements of a 2D Array
Similar to that for 1D array, but use two indices.
  First index indicates row, second index indicates column.
  Both the indices should be expressions which evaluate to integer values.
Examples:
x[m][n] = 0;
c[i][k] += a[i][j] * b[j][k];
val = sqrt( arr[j*3][k+1] );
6
Notes: 37

## Slide 7
How is a 2D array stored in memory?
Starting from a given memory location (starting address of the array), the elements are stored row-wise in consecutive memory locations.
    x: starting address of the array in memory
    c: number of columns
    k: number of bytes allocated per array element, e.g., sizeof(int)
  a[i][j] is allocated memory location at address x + (i * c + j) * k
a[0][0] a[0][1] a[0][2] a[0][3] a[1][0] a[1][1] a[1][2] a[1][3] a[2][0] a[2][1] a[2][2] a[2][3]
Row 0
Row 1
Row 2
7
Notes: 37

## Slide 8
Array Addresses
int main()
{
int a[3][5];
int i, j;
for (i=0; i<3;i++)
{
for (j=0; j<5; j++)
printf ("%u\n", &a[i][j]);
printf ("\n");
}
return 0;
}
3221224480
3221224484
3221224488
3221224492
3221224496
3221224500
3221224504
3221224508
3221224512
3221224516
3221224520
3221224524
3221224528
3221224532
3221224536
Output
8

## Slide 9
How to read the elements of a 2D array?
By reading them one element at a time
for (i=0; i<nrow; i++)
for (j=0; j<ncol; j++)
scanf(“%f”, &a[i][j]);
The ampersand (&) is necessary.
The elements can be entered all in one line or in different lines.
We can also initialize a 2D array at the time of declaration:
int a[MAX_ROWS][MAX_COLS] = { {1,2,3}, {4,5,6}, {7,8,9} };
9
Notes: 37

## Slide 10
How to print the elements of a 2D array?
By printing them one element at a time.
for (i=0; i<nrow; i++)
for (j=0; j<ncol; j++)
printf (“%f ”, a[i][j]);
for (i=0; i<nrow; i++) {
for (j=0; j<ncol; j++)
printf (“%f ”, a[i][j]);
printf(“\n”);
}
10
This will print all elements in one line.
This will print the elements with one row in each line (matrix form).
Notes: 37

## Slide 11
Example: Matrix addition
int main()
{
int a[100][100], b[100][100],
c[100][100], p, q, m, n;
printf (“Enter dimensions: ”);
scanf (“%d %d”, &m, &n);
for (p=0; p<m; p++)
for (q=0; q<n; q++)
scanf (“%d”, &a[p][q]);
for (p=0; p<m; p++)
for (q=0; q<n; q++)
scanf (“%d”, &b[p][q]);
for (p=0; p<m; p++)
for (q=0; q<n; q++)
c[p][q] = a[p][q] + b[p][q];
for (p=0; p<m; p++)
{
for (q=0; q<n; q++)
printf (“%d ”, c[p][q]);
printf (“\n”);
}
return 0;
}
11

## Slide 12
A 2D array means a 1D array of 1D arrays, and so a row pointer
12
#include <stdio.h>
int main ()
{
int i, j, A[4][5] = { { 7, 14, 3, 16, 6}, {11, 5, 9, 13, 18},
{ 2, 15, 20, 1, 19}, {10, 4, 12, 17, 8} };
for (i=0; i<4; ++i) {
for (j=0; j<5; ++j) printf("%p ", &A[i][j]);
printf("\n");
}
printf("sizeof(A) = %3lu, A = %p, A + 1 = %p\n", sizeof(A), A, A + 1);
printf("sizeof(*A) = %3lu, *A = %p, *A + 1 = %p\n", sizeof(*A), *A, *A + 1);
printf("sizeof(&A) = %3lu, &A = %p, &A + 1 = %p\n", sizeof(&A), &A, &A + 1);
return 0;
}
Output
0x7ffc314fe100 0x7ffc314fe104 0x7ffc314fe108 0x7ffc314fe10c 0x7ffc314fe110
0x7ffc314fe114 0x7ffc314fe118 0x7ffc314fe11c 0x7ffc314fe120 0x7ffc314fe124
0x7ffc314fe128 0x7ffc314fe12c 0x7ffc314fe130 0x7ffc314fe134 0x7ffc314fe138
0x7ffc314fe13c 0x7ffc314fe140 0x7ffc314fe144 0x7ffc314fe148 0x7ffc314fe14c
sizeof(A) = 80, A = 0x7ffc314fe100, A + 1 = 0x7ffc314fe114
sizeof(*A) = 20, *A = 0x7ffc314fe100, *A + 1 = 0x7ffc314fe104
sizeof(&A) = 8, &A = 0x7ffc314fe100, &A + 1 = 0x7ffc314fe150
Notes: 37

## Slide 13
Passing 2D arrays to functions
13

## Slide 14
Passing 2D arrays to functions
Similar to that for 1D arrays.
  The array contents are not copied into the function.
  Rather, the address of the first element is passed.
For calculating the address of an element in a 2D array, the function needs:
  The starting address of the array in memory (say, x)
  Number of bytes per element (say, k)
  Number of columns in the array, i.e., the size of each row (say, c)
The above three pieces of information must be known to the function.
a[i][j] is located at memory address x + (i * c + j) * k
14
Notes: 37

## Slide 15
Example
int main()
{
int a[15][25], b[15][25];
…
…
add (a, b, 15, 25);
…
…
}
void add (int x[][25], int y[][25],
int rows, int cols)
{
}
We can also write
int x[15][25], y[15][25];
The first dimension is ignored. But the second dimension must be given.
15

## Slide 16
Example: Matrix addition with functions
void AddMatrix (int A[][100], int B[][100], int C[][100], int x, int y)
{
int i, j;
for (i=0; i<x; i++)
for (j=0; j<y; j++)
C[i][j] = A[i][j] + B[i][j];
}
void ReadMatrix (int A[][100], int x, int y)
{
int i, j;
for (i=0; i<x; i++)
for (j=0; j<y; j++)
scanf (“%d”, &A[i][j]);
}
16

## Slide 17
Example: Matrix addition
int main()
{
int a[100][100], b[100][100],
c[100][100], p, q, m, n;
scanf (“%d%d”, &m, &n);
ReadMatrix(a, m, n);
ReadMatrix(b, m, n);
AddMatrix(a, b, c, m, n);
PrintMatrix(c, m, n);
return 0;
}
void PrintMatrix (int A[][100], int x, int y)
{
int i, j;
printf (“\n”);
for (i=0; i<x; i++)
{
for (j=0; j<y; j++)
printf (“ %5d”, A[i][j]);
printf(“\n”);
}
}
17

## Slide 18
Example:
#include <stdio.h>
int main() {
int a[15][25], b[15][25], c[15][25];
int m, n;
scanf (“%d %d”, &m, &n);
for (p=0; p<m; p++)
for (q=0; q<n; q++)
scanf (“%d”, &a[p][q]);
for (p=0; p<m; p++)
for (q=0; q<n; q++)
scanf (“%d”, &b[p][q]);
add (a, b, m, n, c);
for (p=0; p<m; p++) {
for (q=0; q<n; q++)
printf(“%f ”, c[p][q]);
printf(“\n”);
}
}
void add (int x[][25], int y[][25], int m,
int n, int z[][25])
{
int p, q;
for (p=0; p<m; p++)
for (q=0; q<n; q++)
z[p][q] = x[p][q] + y[p][q];
}
Note that the number of columns has to be fixed in the function definition.
There is no difference between
void add( int x[ ][25], … ) and
void add( int x[15][25], … )
Specifying the first dimension is not necessary, but not a mistake.
17
Notes: 37

## Slide 19
Example: Transpose of a matrix
#include <stdio.h>
void transpose (int x[][3], int n)
{
int p, q, t;
for (p=0; p<n; p++)
for (q=0; q<n; q++)
{
t = x[p][q];
x[p][q] = x[q][p];
x[q][p] = t;
}
}
main()
{
int a[3][3], p, q;
for (p=0; p<3; p++)
for (q=0; q<3; q++)
scanf (”%d”, &a[p][q]);
transpose (a, 3);
for (p=0; p<3; p++)
{
for (q=0; q<3; q++)
printf (”%d ”, a[p][q]);
printf (“\n”);
}
}
19

## Slide 20
Example: Transpose of a matrix
#include <stdio.h>
void transpose (int x[][3], int n)
{
int p, q, t;
for (p=0; p<n; p++)
for (q=0; q<n; q++)
{
t = x[p][q];
x[p][q] = x[q][p];
x[q][p] = t;
}
}
This transpose function is wrong. Why?
20
main()
{
int a[3][3], p, q;
for (p=0; p<3; p++)
for (q=0; q<3; q++)
scanf (”%d”, &a[p][q]);
transpose (a, 3);
for (p=0; p<3; p++)
{
for (q=0; q<3; q++)
printf (”%d ”, a[p][q]);
printf (“\n”);
}
}

## Slide 21
The Correct Version
void transpose (int x[][3], int n)
{
int p, q, t;
for (p = 0; p < n; p++)
for (q = p; q < n; q++)
{
t = x[p][q];
x[p][q] = x[q][p];
x[q][p] = t;
}
}
10 20 30
40 50 60
70 80 90
10 40 70
20 50 80
30 60 90
21
You may start the inner loop with q = p + 1

## Slide 22
21
Note
We have done static allocation of 1D / 2D arrays. Dynamic allocation will possibly be covered later.
We have studied 1D and 2D arrays only. C allows arrays of higher dimensions as well.
For example, int a[10][15][20] is a 3D array (not in syllabus).

## Slide 23
Practice problems
Write a function that takes an n x n square matrix A as parameter (n < 100) and returns 1 if A is an upper-triangular matrix, 0 otherwise.
Repeat 1 to check for lower-triangular matrix, diagonal matrix, identity matrix.
Consider an n x n binary matrix (contains only 0 or 1). Write a function that takes such a matrix and returns 1 if the number of 1’s in each row are the same and the number of 1’s in each column are the same; it returns 0 otherwise.
Write a function that reads in an m x n matrix A and an n x p matrix B, and returns the product of A and B in another matrix C. Pass appropriate parameters.
Write a function to find the transpose of a non-square matrix A in a matrix B.
Repeat the last exercise when the transpose of A is computed in A itself. Use no additional 2D arrays.
For each of the above, also write a main function that reads the matrices, calls the function, and prints the results (a message, the result matrix, etc.)
23

## Slide 24
ADVANCED TOPICS
Pointers equivalent to twoDimensional arrays
24
Notes: 37

## Slide 25
Generalization from oneDimensional arrays
Consider the statically allocated 1D array:
int A[20];
A pointer that can browse through A is declared as:
int *p;
Such a pointer can be allocated dynamic memory and freed as:
p = (int *)malloc(20 * sizeof(int));
free(p);
What are the analogous pointers for 2D arrays that you have seen earlier?
How can these pointers be allocated and deallocated their own memory?
25
Notes: 37

## Slide 26
What are our 2D arrays?
We have seen two types of 2D arrays:
int A[10][20];
int *B[10];
Both these arrays are statically allocated.
A is an array of arrays, and has no dynamic component.
B is an array of pointers. Individual pointers in B[] can be dynamically allocated.
As statically allocated arrays, both A and B suffer from the two standard disadvantages:
Waste of space
Inadequacy to handle larger than the allocated space
Dynamic versions of A and B overcome these shortcomings.
26
Notes: 37

## Slide 27
Dynamic version of A
int A[10][20];
A pointer matching A should be a pointer to an array of 20 int variables.
But
int *p[20];
declares an array of 20 int pointers, not a pointer to an array.
Three ways of defining the correct pointer equivalent to A:
Method 1: int (*p)[20];
Method 2: typedef int row[20];
row *p;
Method 3: typeof(int [20]) *p; // Not available in the original C specification
In all the cases, p is a single pointer.
27
Notes: 37

## Slide 28
Dynamic version of B
int B[10];
B is an array of 10 int pointers.
The equivalent pointer is a pointer to an int pointer.
int **q;
A 2D array declared by q is fully dynamic.
The number of rows can be decided during the run of the program.
The size of each row can also be decided individually during the run.
Note: It is illegal to set q = A; or p = B; Expect segmentation fault if you do so (ignoring the warnings issued by the compiler).
28
Notes: 37

## Slide 29
Dynamic memory for p
p is a single pointer, and can be allocated and deallocated memory in a single shot.
Method 1:
p = (int (*)[20])malloc(10 * 20 * sizeof(int));
Method 2:
p = (row *)malloc(10 * sizeof(row));
Method 3:
p = (typeof(int [20]) *)malloc(10 * 20 * sizeof(typeof(int [20])));
Freeing requires only one call.
free(p);
29
Notes: 37

## Slide 30
Dynamic memory for q
First, you allocate the required number of row headers, and then the rows individually.
q = (int **)malloc(10 * sizeof(int *));
for (i=0; i<10; ++i)
q[i] = (int *)malloc(20 * sizeof(int));
Freeing is also a multi-step process.
for (i=0; i<10; ++i) free(q[i]);
free(q);
Note: Free the individual rows before freeing the array of row headers.
30
Notes: 37

## Slide 31
A Vandermonde matrix corresponding to n real-valued elements a0, a1, …, an-1 is defined as:
An application works with Vandermonde matrices for n ≤ 100. A static 2D array would require a total storage of 100 x 100 = 10,000 cells. This leads to waste if n is small.
We write a function genvdm(A,n) that obtains a0, a1, …, an-1 from the 1D array A, and returns a pointer to a dynamically allocated array of rows.
The row size must be fixed beforehand. But we can allocate exactly n rows to reduce wastage.
Example: Vandermonde matrices
31
1 | 1 | 1 | … | 1
a0 | a1 | a2 | … | an-1
a02 | a12 | a22 | … | an-12
⋮ | ⋮ | ⋮ | … | ⋮
a0n-1 | a1n-1 | a2n-1 | … | an-1n-1
Notes: 37

## Slide 32
Dynamic memory for storing Vandermonde matrices
#include <stdio.h>
#include <stdlib.h>
#define MAXDIM 100
double (*genvdm ( double *A, int n )) [MAXDIM]
{
double (*p)[MAXDIM];
int i, j;
p = (double (*)[MAXDIM])malloc(n * MAXDIM * sizeof(double));
for (i=0; i<n; ++i) {
// i is an index in A, and a column in p. j is a row in p.
p[0][i] = 1;
for (j=1; j<n; ++j) p[j][i] = p[j-1][i] * A[i];
}
return p;
}
void prnvdm ( double M[][MAXDIM], int n )
{
int i, j;
for (i=0; i<n; ++i) {
for (j=0; j<n; ++j) printf("%10.5lf ", M[i][j]);
printf("\n");
}
}
32
Notes: 37

## Slide 33
Storage of Vandermonde matrices (continued)
int main ()
{
double A[MAXDIM], (*V)[MAXDIM];
int n, i;
printf("Enter dimension of V: "); scanf("%d", &n);
printf("Enter %d elements: ", n);
for (i=0; i<n; ++i) scanf("%lf", A+i);
V = genvdm(A,n);
prnvdm(V,n);
exit(0);
}
33
Output
Enter dimension of V: 5
Enter 5 elements: -1 0.1 1.1 2.5 3.2
1.00000 1.00000 1.00000 1.00000 1.00000
-1.00000 0.10000 1.10000 2.50000 3.20000
1.00000 0.01000 1.21000 6.25000 10.24000
-1.00000 0.00100 1.33100 15.62500 32.76800
1.00000 0.00010 1.46410 39.06250 104.85760
Exercise: Free the 2D memory allocated to V.
Notes: 37

## Slide 34
Antisymmetric matrices
A symmetric matrix is an n x n matrix with aij = aji for all i, j.
An antisymmetric matrix is an n x n matrix with aij = –aji for all i, j. Since aii = –aii , the main diagonal is filled by 0. Moreover, the entries below the main diagonal can be obtained from the entries above the main diagonal.
We can use a fully dynamic 2D array to store only the elements above the main diagonal.
34
0 | 5 | 3 | –2 | 4
–5 | 0 | –6 | –1 | 0
–3 | 6 | 0 | 2 | 7
2 | 1 | –2 | 0 | 1
–4 | 0 | –7 | –1 | 0
Notes: <number>

## Slide 35
Compact storage of an antisymmetric matrix
#include <stdio.h>
#include <stdlib.h>
int **genasm ( int n )
{
int **q, i, j;
q = (int **)malloc((n-1) * sizeof(int *));
for (i=0; i<n-1; ++i) {
q[i] = (int *)malloc((n-i-1) * sizeof(int));
for (j=i+1; j<n; ++j) q[i][j-i-1] = i-j;
}
return q;
}
35
The function genasm(n) returns a pointer to the “array” given n as input. Let us take aij = i – j.
Notes: <number>

## Slide 36
Storage of antisymmetric matrices (continued)
void prnasm ( int *U[], int n )
{
int i, j;
for (i=0; i<n; ++i) {
for (j=0; j<i; ++j) printf("%3d ", -U[j][i-j-1]);
printf(" 0 ");
for (j=i+1; j<n; ++j) printf("%3d ", U[i][j-i-1]);
printf("\n");
}
}
int main ()
{
int **U, n;
printf("Enter dimension (n): "); scanf("%d", &n);
U = genasm(n);
prnasm(U,n);
exit(0);
}
36
Output
Enter dimension (n): 5
0 -1 -2 -3 -4
1 0 -1 -2 -3
2 1 0 -1 -2
3 2 1 0 -1
4 3 2 1 0
Exercise: Free the 2D memory allocated to U.
Notes: <number>

## Slide 37
Four types of 2D arrays
37
Declaration | Number of rows | Number of columns
int A[10][20]; | Static | Static
int (*p)[20]; | Dynamic | Static
int *B[10]; | Static | Dynamic
int **q; | Dynamic | Dynamic
Notes: <number>