## Slide 1: Deadlock-free Packet Switching
CS60002: Distributed Systems
Pallab Dasgupta
Professor,
Dept. of Computer Sc. & Engg.,
Indian Institute of Technology Kharagpur

## Slide 2: Store and forward deadlock
s
t
u
v
Buffer-size = 5
Node s sending 5 packets to v through t
Node v sending 5 packets to s through u

## Slide 3: Model
The network is a graph G = (V, E)
Each node has B buffers
Moves:
Generation. A node u creates a new packet p and places it in an empty buffer in u. Node u is the source of p.
Forwarding. A packet p is forwarded from a node u to an empty buffer in the next node w on its route.
Consumption. A packet p occupying a buffer in its destination node is removed from the buffer.

## Slide 4: Requirements
The packet switching controller has the following requirements:
  The consumption of a packet (at its destination) is always allowed.
  The generation of a packet in a node where all buffers are empty is always allowed.
  The controller uses only local information, that is, whether a packet can be accepted in a node u depends only on information known to u or contained in the packet

## Slide 5: Solutions
Structured solutions
    Buffer-graph based schemes
      The destination scheme
      The hops-so-far scheme
      Acyclic orientation based scheme
Unstructured solutions
    Forward count and backward count schemes
    Forward state and backward state schemes

## Slide 6: Buffer Graph
A buffer graph (for, G, B) is a directed graph BG on the buffers of the network, such that
  BG is acyclic (contains no directed cycle);
  bc is an edge of BG if b and c are buffers in the same node, or buffers in two nodes connected by a channel in G; and
  for each path   P there exists a path in BG whose image is .
      P is the collection of all paths followed by the packets – this collection is determined by the routing algorithm.

## Slide 7: Suitable buffer and guaranteed path
Let p be a packet in node u with destination v.
    A buffer b in u is suitable for p if there is a path in BG from b to a buffer c in v, whose image is a path that p can follow in G.
    One such path in BG will be designated as the guaranteed path and nb(p, b) denotes the next buffer on the guaranteed path.
    For each newly generated packet p in u there exists a designated suitable buffer, fb(p) in u.

## Slide 8: The buffer-graph controller
A buffer-graph controller decides how packets are routed through the BG.
Requirements
The generation of a packet p in u is allowed iff the buffer fb(p) is free. If the packet is generated it is placed in this buffer.
The forwarding of a packet p from a buffer in u to a buffer in w is allowed iff nb(p, b) (in w) is free. If the forwarding takes place p is placed in nb(p, b).
The buffer-graph controller is a deadlock-free controller.

## Slide 9: The Destination Scheme
Uses N buffers in each node u, with a buffer bu[v] for each possible destination v
    It is assumed that the routing algorithm forwards all packets with destination v via a directed tree Tv rooted towards v.
  The buffer graph is defined by BG = (B, E), where bu[v1]bw[v2]  E iff v1 = v2 and uw
  is an edge of Tv1.
There exists a deadlock-free controller for arbitrary connected networks that uses N
buffers in each node and allows packets to be routed via arbitrarily chosen sink trees

## Slide 10: The Hops-so-far Scheme
Node u contains k + 1 buffers bu[0], …, bu[k].
It is assumed that each packet contains a hop-count indicating how many hops the packet has made from its source
  The buffer graph is defined by BG = (B, E), where bu[i]bw[j]  E iff i + 1 = j and uw is an edge of the network.
  There exists a deadlock-free controller for arbitrary connected networks that uses D+1 buffers in each node (where D is the diameter of the network), and requires packets to be sent via minimum-hop paths.

## Slide 11: Acyclic Orientation based Scheme
Goal: To use only a few buffers per node
An acyclic orientation of G is a directed acyclic graph obtained by directing all edges of G
A sequence G1, …, GB of acyclic orientations of G is an acyclic orientation cover of size B for the collection P of paths if each path   P can be written as a concatenation of B paths 1, …, B, where I is a path in Gi.
    A packet is always generated in node u in buffer bu[1]
    A packet in buffer bu[i] that must be forwarded to node w is placed in buffer bw[i] if the edge between u and w is directed towards w in Gi, and to bw[i + 1] if the edge is directed towards u in Gi.
If an acyclic orientation cover for P of size B exists, then there exists a deadlock-free
controller using only B buffers in each node.

## Slide 12: Forward and Backward-count Controllers
Forward-count Controller:
For a packet p, let sp be the number of hops it still has to make to its destination (0  sp  k)
For a node u, fu denotes the number of free buffers in u (0  fu  B)
The controller accepts a packet p in node u iff sp < fu.
If B > k then the above controller is a deadlock-free controller
Backward-count Controller:
For a packet p, let tp be the number of hops it has made from its source
The controller accepts a packet p in node u iff tp > k – fu.

## Slide 13: Forward and Backward-state Controllers
Forward-state Controller:
For a node u define (as a function of the state of u) the state vector as (j0, …, jk), where js is the number of packets p in u with sp = s.
The controller accepts a packet p in node u with state (j0, …, jk) iff:
If B > k then the above controller is a deadlock-free controller
Backward-state Controller:
Define the state vector as (i0, …, ik), where it is the number of packets in node u that have made t hops.
The controller accepts a packet p in node u with state (i0, …, ik) iff:

## Slide 14: Forward-state versus Forward-count
Forward-state controller is more liberal than the forward-count controller
Every move allowed by the forward-count controller is also allowed by the forward-state controller